## Slide 1: 实验10 FSM——有限状态机
实验目标
  了解两段式、三段式有限状态机的写法
  掌握Mealy型有限状态机建模方法
  掌握Moore型有限状态机建模方法
  学会使用有限状态机进行时序控制

## Slide 2: 实验要求
1-1 使用三段式Mealy型FSM实现一个序列检测器，当接收到的1的总数为3的整数倍时，输出为1，否则输出0。编写代码2分、仿真2分、下载2分。
2-1 使用三段式Moore型FSM实现一个序列检测器，序列为01/00时输出为0，序列为11/00时输出为1，序列为10/00时输出反转，否则输出保持不变。编码2分、仿真2分、下载2分

## Slide 3: 仿真波形
1-1 序列检测
2-1 序列检测

## Slide 4: Mealy型FSM
两段式
三段式

## Slide 5
module mealy_2 (input clk, input reset, input x, output reg parity);
reg state, nextstate;
parameter S0=0, S1=1;
always @(posedge clk or posedge reset) // always block to update state
if (reset) state <= S0;
else state <= nextstate;
// always block to compute both output & nextstate
always @(*)
begin
  parity = 1'b0;
  case(state)
    S0: if(x) begin parity = 1; nextstate = S1; end
    else nextstate = S0;
    S1: if(x) nextstate = S0;
    else begin parity = 1; nextstate = S1; end default: nextstate = S0;
  endcase
end endmodule

## Slide 6: Moore FSM
结构图
状态转移图
  奇偶校验

## Slide 7
module moore_3 (input clk, input reset, input x, output reg parity);
reg state, nextstate; parameter S0=0, S1=1;
always @(posedge clk or posedge reset) // always block to update state if (reset) state <= S0;
  else state <= nextstate;
always @(*) // always block to compute nextstate
  begin
    nextstate = S0;
    case(state)
      S0: if(x) nextstate = S1;
      S1: if(!x)nextstate = S1;
    endcase
  end
endmodule
always @(state) // always block to compute output
  begin
    case(state) S0: parity = 0; S1: parity = 1; endcase
  end